## Slide 1: INF142: Kræsjkurs

## Slide 2: Informasjon
Jenny og Fredrik
Norsk
Opplegg
  45 min gjennomgang
  15 min pause
Ta egne notater!!!
Quiz 1
Værstasjon
Quiz 2
Eksamen
10 %
20 %
10 %
60 %

## Slide 3: Innhold
Delay
Lag arkitekturen (m/ protokoller)
Innkapsling
Socket programming
Oppgave gjennomgang
Spørsmål

## Slide 4: Delay
Processing delay:
  Tiden som kreves for å undersøke pakkens «header», hvor man skal videresende pakket etc.
  I høy-hastighets rutere tar prosesseringen bare mikrosekunder (denne blir ofte ignorert)
Queuing delay:
  Tiden som pakken bruker i køen.
  Mikrosekunder til millisekunder.
  Funksjon av pågangen

## Slide 5: Delay
Transmission delay:
  Tiden som kreves for å dytte alle bitsene til pakken innpå linken
  Mikrosekunder til millisekunder

## Slide 6: delay
Propagation delay:
  Tiden det tar for en bit å «propegate» gjennom linken.
  Avhenger av avstand mellom rutere og «propagation» fart til linken.

## Slide 7: Total nodal delay
Summen av alle «total nodal delays» i nodene som blir brukt i overføringen.
End to end delay

## Slide 8: Kahoot

## Slide 9: Application layer
Inneholder nettverksapplikasjonene
Inneholder protokollene:
HTTP
SMTP
DNS
Enhet: Message
Application

## Slide 10: Transport layer
Transporterer applikasjon-lag meldinger mellom applikasjons-endepunkter
Inneholder protokollene:
TCP
UDP
Enhet: Segment
Transport

## Slide 11
UDP
  Identify
    IP address (Destination)
    Port number (Destination)
TCP (forbindelses orientert)
  A four-tuple:
    IP address (Source)
    Port number (Source)
    IP address (Destination)
    Port number (Destination)

## Slide 12: Header fields (TCP)
Length
It specifies the length in bytes of the udp header and UDP data. The minimum length is 8 bytes.
Payload:
The limit for the data length is imposed by the underlying network-layer protocol
Checksum
It is used for error-checking if the header and data.
It is optional in IPv4 and mandatory in IPv6
The field carries all-zeroes if unused
Sequence number
Acknowledgement number
Data offset:
Specifies the size of the TCP header in 32-bit words. The minimum size is 5 words and the maximum is 15 words.
Reserved
Block of bits that are reserved (0)
Flags:
Contains 9 bits. Some flags:
ACK: used to indicate that the value carried in the acknowledgement field is valid.
RST, SYN, FIN: used for connection setup and teardown.
CWR, ECE: used in explicit congestion.
Window size:
Specifies the number of window size until the sender of this segment is currently willing to receive.
Urgent pointer
If the URG flag is set, then this 16-bit field is an offset from the sequence number indicating the last urgent data byte.
Options
Option-Kind (1 byte)
Option-Length (1 byte)
Option-Data (variable)
Header fields (UDP)

## Slide 13: Network layer
Flytter nettverks-lag pakker fra Host A til Host B
Inneholder protokollene:
IP
Routing protokoller
Enhet: Datagram
Network

## Slide 14: IP
Beste innsats leveringssystem
IKKE pålitelig datalevering

## Slide 15: Link layer
Flytter pakker gjennom linker, node til node
Enhet: Frame
Link

## Slide 16: Physical layer
Flytter enkelte «bits» fra node til node
Enhet: Bit
Physical layer

## Slide 17: Lagdelt arkitektur
Application
Transport
Network
Link
Physical
HTTP
SMTP
DNS
TCP
UDP
IP
Frame
Message
Segment
Datagram
Bit
Lag
Protokoller
Enhet
1.
2.
3.
4.
5.

## Slide 18: Innkapsling (Encapsulation)
Hva er innkapsling?
Hvorfor trenger vi det?

## Slide 19: Innkapsling (Encapsulation)
Application
Transport
Network
Link
Physical
data
data
data
data
- Message
- Segment
- Datagram
- Frame
- Bits

## Slide 20: Socket programming
Server
Client

## Slide 21: Kahoot

## Slide 22: Oppgave gjennomgang

## Slide 23: GS10: Oppgave 6
1) Task 6 Consider a router that interconnects three subnets: Subnet 1, Subnet 2, and Subnet 3. Suppose all of the interfaces in each of these three subnets are required to have the prefix 223.1.17/24. Also suppose that Subnet 1 is required to support up to 62 interfaces, Subnet 2 is to support up to 106 interfaces, and Subnet 3 is to support up to 15 interfaces. Provide three network addresses (of the form a.b.c.d/x) that satisfy these constraints.

## Slide 24
Sjekk
#
0
1
1
0
/25
/24
/26
a.b.c.0/25
a.b.c.192/26
a.b.c.128/26
128 + 64 = 192
0 + 128 = 128

## Slide 25
To addresser er reservert
  Nettverksadressen = 1...1
  Kringkasteadressen = 0...0
adresser dekker behovet
adresser dekker behovet
adresser dekker behovet

## Slide 26: Quiz 1: Spørsmål 4
Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has three links, of rates
{ R1 = 500 kbps, R2 = 600 kbps, R3 = 1 Mbps }
Assuming there is no other traffic in the network, what is the throughput for the file transfer?
0,5 Mbps
1 Mbps
0,6 Mbps

## Slide 27: Quiz 1: Spørsmål 13
Hosts A and B are directly connected by a link whose transmission rate is 3,0 Mbps and propagation delay is 4,2 ms. Host A is sending a huge file continuously (assume that the file is sent as one big packet). What is the maximum number of bits traveling through the link at any given time while the transfer lasts?

## Slide 28: Quiz 1: Spørsmål 14
A user is directly connected to a server through a twisted-pair cable for transmitting a 1500-bytes file. The transmission rate is 3 Mbps and the propagation speed is 105 km/s. Suppose that the file will be transmitted as a whole in one packet without headers. Assuming that the user is located 4 x 105 m away from the server and ignoring processing and queuing delay, compute the nodal delay in ms.

## Slide 29: Quiz 2: Spørsmål 1 og 5
Select the subnet mask of 172.31.192.0/24.
An 𝑁-bit ones' complement system can only represent integers in the range −𝑘 to 𝑘, where 𝑘 is computed by using 𝑁. Knowing that 𝑁= 7, what is the value of 𝑘?

## Slide 30: GS9: Problem 7
Consider the following tiny-UDP packet:
  Verify the checksum.
10011001 11100010 00100100 10000100

## Slide 31: GS10: Oppgave 5
An 40-byte message gets encapsulated into a TCP segment which in turn gets encapsulated into an IPv4 datagram.
What percentage of this datagram will be overhead, and what percentage will be application data? (Assume that the Options fields are not being used)
The size of the TCP (Transmission Control Protocol) header = 20 bytes
The size of the IP header = 20 bytes
50 %

## Slide 32: GS11: Oppgave 9
Using Dijkstra’s algorithm, find the least-cost path from v to every node in the following graph.

## Slide 33: Kapittel 1: Problem 10
Consider a packet of length which begins at end system A and travels over three links to a destination end system. These three links are connected by two packet switches. Let , , denote the length, propagation speed, and the transmission rate of link , for . The packet switch delays each packet by d proc. Assuming no queuing delays, in terms of , , , , and , what is the total end-to-end delay for the packet?
Suppose now the packet is , the propagation speed on all three links is , the transmission rates of all three links are 2 Mbps, the packet switch processing delay is , the length of the first link is , the length of the second link is , and the length of the last link is . For these values, what is the end-to-end delay?
(Fra Computer Networking: A Top Down Approach)

## Slide 34: GS2: Oppgave 5
Host A and Host B are connected by a link whose transmission rate is 8 Mbps and propagation delay is 10 ms. In a video call, Host A encodes video at 5 Mbps. Then, Host A groups the resulting bits into 1500-byte packets (assume that these packets do not have a header and that they are neither encapsulated nor split into other packets). As soon as Host A gathers a packet, it sends the packet to Host B. How much time elapses (in ms) from the time the first bit is created (because of the encoding at Host A) until Host B receives the first packet?

## Slide 35: Kahoot

## Slide 36: spørsmål